## Slide 1: Verification
Spring 2021
Tufts University
Instructors: Joel Grodstein, Scott Taylor
joel.grodstein@tufts.edu
Introduction

## Slide 2: Typical schedule
Which milestone is most “important?”
  If your definition of “important” includes the company staying afloat…
  “time to other peoples’ money”
  Customers really, really dislike giving you money for a broken product!
  Silicon spins take lots of time
Tapeout 1
Tapeout 2
sales
all units coded
top-level assembled
concepts done
small team moves to next project
huge team comes onboard
team leaders write a paper
Notes: Customers don’t pay you for writing beautiful papers… unfortunately.
Message – you had better not tape out with lots of bugs!

## Slide 3: What’s in this lecture
The course – once quickly
Why do we care about verification?
What is a verification engineer?
What we’ll learn
Resources
Notes: The format of the course is the coronavirus version!

## Slide 4: What is verification?
Trying to find the bugs in a design
You’ve found your own bugs in your own designs
  probably hasn’t been easy
  gets exponentially worse for larger designs 
Verification is a separate specialty
  Typically more verification engineers than design engineers!
  And design engineers spend over half their time in verification

## Slide 5: Instructor
Instructor: Joel Grodstein
Office Hours:
  TBD
Background
  30 years in the semiconductor industry
  2nd career as a half-time lecturer here

## Slide 6: Instructor
Instructor: Scott Taylor
Office Hours:
  TBD
Background
  28 years in the semiconductor industry, mostly in verification
  15 years at Intel, currently at Nvidia (5 years)
  Currently on CPU verification for self-driving cars
  Principal engineer
  Doing this course for the fun of it
  They pay me to break things 

## Slide 7: Prerequisites
Ability to program with a Hardware Description Language
  We’ll be using SystemVerilog
  VHDL is fine
  C++ is actually fine, too
Basic computer architecture
  Understand what gates, flops, clocks, memories are (ES4)
  Understand what a pipeline is, basic CPU arch (EE126)
Attitude
  You like to break things
  You enjoy detective work
  You enjoy automating stuff
  Mix of HW and SW
Notes: Note the CPU architecture is more for the examples than anything else; we’ll be building a router, not a CPU

## Slide 8: Course format
Work in small groups
  2-3 people
  can stay in your group or occasionally re-form
Programming assignments
  write our own FIFO & mesh (or parts of them)
  write parts of our own testbench(es)
  debug derby at the end
Oral group quizzes

## Slide 9: Hybrid
Mix of styles
Some topics are synchronous
  traditional classroom but via Zoom; one or two breaks
Some topics are flipped
  5-10 minute videos
  Small-group (≈3-6 people) discussions, any questions
Other activities
  oral group quizzes
  debug/etc. help
  during office hours (or class slots when flipped)
All virtual at first
  Small-group could move to outdoors in warmer weather (not Scott)

## Slide 10: Goals for week 1
Course website
  https://www.ece.tufts.edu/ee/165/
  Most everything except grades
Communications?
  Slack? Discord? Campuswire? Other?
Feedback on class format
Form small groups
  Sign up for any small-group meeting slots if you like

## Slide 11: What’s in this lecture
The course – once quickly
Why do we care about verification?
What is a verification engineer?
What we’ll learn
Resources
Notes: The format of the course is the coronavirus version!

## Slide 12: First claim
Verification is a big (and getting bigger) job market

## Slide 13: Job statistics
2020 Wilson Group Verification Study
  full 1-hour video at https://verificationacademy.com/seminars/2020-functional-verification-study
Notes: You must register to get the video (free registration).
Surveyed 1500 people (across all major EDA companies).
Crossover point where more verif. engineers than design happened in 2014.

## Slide 14
CAGR for verif(design) is 5.5%(1.5%) from 2012-2020
47% of design-eng time is spent in verif, 53% in design
Notes: Remind them what CAGR stands for

## Slide 15: Why so many verif. engs?
Which milestone is most “important?”
  If your definition of “important” includes the company staying afloat…
  “time to other peoples’ money”
  Customers really, really dislike giving you money for a broken product!
  Silicon spins take lots of time
Tapeout 1
Tapeout 2
all units coded
top-level assembled
concepts done
small team moves to next project
huge team comes onboard
team leaders write a paper
sales
Notes: This is a duplicate of slide #2 – emphasizing that the way to improve time to other peoples’ money is to *not* have 10 tapeouts.
In other words, verify!
That’s why verification is financially necessary.

## Slide 16: Cost of a bug fix
Early in design: 1 engineer week ($5K)
Late in design: 1 week tapeout slip = $2M
  or 1 week = 1% performance
Post-silicon: 1 extra tapeout ($+2 months) = $20M
Post-FRS: lose 20% of your customers = $20M/year
After substantial field volume: recalls
  1995 Pentium fix = $495M
400x
4000x
100,000x
Notes: Assume you’re selling a GPU; 1M units/year, $100/unit. so $100M/year or $2M/week
Hard to compute the cost of a tapeout (depends on your volume, etc and how many layers it involves). Scott’s numbers are $1M/layer, or $40M for a full-layer tapeout and $20M for metal-only. I’ll use $50M since Scott’s numbers are slightly old.

## Slide 17: Design trends
Increasing use of multicore, SOC
  designers “just” assemble existing pieces
  harder than it sounds, but still!
  lots of individual pieces → large cross-product space to verify
Notes: I.e., this is another reason why verification teams are growing faster than design teams

## Slide 19
Notes: Extra spins are of course much cheaper and faster with FPGAs, which changes the economics a lot. But silicon debug is still lots harder than debugging a failed verification test, due to the reduced visibility. So the message is that without sufficient pre-silicon verification, you still get customer bugs.

## Slide 20: Errata
Errata happen all the time
Intel Core 8th and 9th gen (Coffee Lake)
  137 errata in released chips
  https://www.intel.com/content/dam/www/public/us/en/documents/specification-updates/8th-gen-core-spec-update.pdf

## Slide 21: Why so many escapes?
Why don’t those idiots get things right the first time?

## Slide 22
Notes: Here’s why those idiots don’t get it right the first time!

## Slide 23
Notes: And this too!

## Slide 25
Notes: Yes, design errors are the most common escape to silicon. But spec changes happen all the time – and as the worlds keeps changing quickly, specs become more and more fluid.

## Slide 26: What’s in this lecture
The course – once quickly
Why do we care about verification?
What is a verification engineer?
What we’ll learn
Resources
Notes: The format of the course is the coronavirus version!

## Slide 27: What is verification?
Or – what isn’t it? 
Is it…
  finding ALL the bugs?
  proving that there are NO bugs?
  guaranteeing production-ready first silicon?
  showing that we've eliminated the likely sources of bugs that may block silicon bringup?
more on Formal later…
life doesn’t come with guarantees 
good luck with that goal!

## Slide 29: Verification skills
Verification requires a jack-of-all-trades
  we now call it diversity of skills 
Architecture design, HW design
  To understand the thing you’re writing tests for!
Software skills
  20% of time spent in testbench development
Debug skills
  41% of your time 
Paranoia
  must think what’s most likely to break
Levelheaded
  You are the agent of turmoil

## Slide 31: Evolution of verification
The “good old days”
  designs were relatively simple
  everyone “verified” their own work
  and it usually worked fine!
But then designs got more complex
  Billions of transistors, numerous clock domains, embedded CPUs, …
  Too many tests to write
  Specialized infrastructure and skills are needed
  And so… specialists are needed!
Realization: verifying your own design is a bad idea
  We humans are really bad at finding our own flaws
Notes: Nvidia Ampere = over 50 billion transistors

## Slide 32: War stories

## Slide 33: Pentium FDIV bug
Oct 19, 1994 discovered by Thomas Nicely
Oct 24: reported to Intel
  previously discovered (but not publicized) by Intel
Oct 30: reported to friends for independent confirmation
Nov 7 EE Times article
Nov 21 CNN article
  Intel offers to replace parts for users who can show they were “affected”
  Public outcry; IBM joins condemnation
Dec 1994: Intel replaces for “all users who request it”
Jan 1995: $495M charge against earnings ($750M today)
Background: Intel had gone from a no-name PC-component supplier to starting “Intel Inside” in 1991
Notes: The original bug find was by Tom Kraljevic, a Purdue intern student working for Intel in Hillsboro! But Intel never made it public (or so says Wikipedia).
Yes, the half-billion dollar charge was from, according to Wikipedia, “only a small fraction of users” requesting replacement CPUs.
Did they mishandle the issue? Perhaps. They were learning how big, famous companies must behave!
The motto – if you’re successful and you make money – then everyone wants a piece of you.

## Slide 34: Spectre / Meltdown
Ways to exploit hardware security holes
The holes have been in CPU hardware for many years
Nobody thought of them until recently – why not?
  Thousands of verification engineers, and nobody wrote the right test 
  Again: verification doesn’t prove the design works perfectly!
Notes: OK, that’s quite an oversimplification of why the bugs slipped through for so long! Scott’s more detailed story is that back in the day, the existence of possible side channels was known at Intel. But that was before the advent of a user-accessible fine-grained timer, so Intel (correctly) concluded that there was no way to exploit the problem, and proceeded to forget all about it. Then later they did add a fine-grained times and forgot that there would be consequences! (It’s even a bit more complex than this; I think there was another dependency or two in addition to the fine-grained timer).

## Slide 35: Intel server reset bug
Nearly all chips need to be reset
How hard is it to get reset right?
  Really hard!
  Multiple clock domains, voltage domains, turning on power supplies and clocks…
Bug in clock crossing hardware
  Chips would not come out of reset
  Lots of on-die debugging logic; almost none of it would function during reset!
  4 weeks of frantic all-hands-on-board debug found a lousy workaround
  fixed on second tapeout
Notes: This is from an unspecified server chip .

## Slide 36: What’s in this lecture
The course – once quickly
Why do we care about verification?
What is a verification engineer?
What we’ll learn
Resources

## Slide 37: Skills we’ll learn
Learn how to verify a register-transfer level (RTL) description of a chip
Learn a verification mindset
Understand the business of verification
Learn about the life of a verification engineer
Learn SystemVerilog
Notes: By the end of the course, this is what we’ll know

## Slide 38: Topics in order
Intro to verification and the course (this lecture!)
Intro to SystemVerilog and a FIFO
Understanding a design
Verification concepts
Developing a test plan
Testbenches
The mesh
Stimulus: directed vs. random tests
Correctness: knowing if your test passed
Coverage

## Slide 39: Big words
A testplan lists:
  what to test
  how to test it
  what’s your infrastructure
  resources needed
A testbench includes
  Your drivers, monitors, checkers, scoreboards, …

## Slide 40: Types of tests
Directed test
  A test, typically written by hand, to test a specific feature with a specific (typically) hand-chosen stimulus
Random-code generator
  Like the name says!
  Generate tons of random input
Pros and cons of each?
  An RCG can generate lots of tests, fast!
  And you test stuff you never thought of
  But how do you know what the right answer is?
  How do you know if you’ve tested a given feature?

## Slide 41: Intro to SystemVerilog
This is not primarily a language course
  it’s about learning verification concepts
But SV is:
  overwhelmingly used in verification
  underwhelmingly taught at universities
How we’ll learn it:
  videos on the basics, and on common mistakes
  Spear textbook has more
  Learn by doing; from simple stuff to harder
  We’re here for questions!
Our running examples are all in SV, as is the testbench
Verification code in industry is heavily object-oriented

## Slide 46: Formal verification
Mathematical proofs that the design does X
X may be
  two mux selects are never on in the same cycle
  floating-point multiplier gives correct answer for all inputs
  or most anything else
  can be great when it succeeds 
  requires expertise to get it to succeed 

## Slide 47: Debug-derby rounds
Everyone will code (flesh out)
  design (FIFO + mesh)
  testbench pieces, including an RCG
First test your design with your own testbench
  then trade with other people
  running their tests on your design
  multiple rounds

## Slide 48: Bugs are good!
How do we know when a design is ready to tape out?
bug count
time
The faster you find bugs up front, the faster you can finish!
  As noted: fixing bugs early is relatively cheap
  The bugs are there; finding them is good
  When you find a bug, shout it from the rooftops!

## Slide 49: Example #1: FIFO
Items go in… come out in the same order
May make it asynchronous
Why is asynch harder?
rst
rd_en
rd_clk
clk
rd_data
wr_en
wr_data
empty
full
wr_clk

## Slide 50: Example #2: mesh routing fabric
Main design for this course: a mesh
  N x N grid of mesh stops (MS)
  A MS can accept a packet from the environment
  Fabric routes packets to their destination MS
00
01
02
03
10
11
12
13
20
21
22
23
30
31
32
33

## Slide 51: What we won’t cover
This is just an introductory course
Lots of formal verification
UVM (Universal Verification Methodology)
  Almost universally used
  We’ll run out of time to cover it
  But you’ll know enough to pick it up quite quickly if you use it on the job

## Slide 53: The rest of the course
We know the problem to be solved
  Just find the mistakes that the design team overlooked
  Bigger, more complex designs → problem will get worse, not better
We know the names of the technologies we will use
What’s left
  learn them
  apply them
  hone your spidey sense 

## Slide 54: What’s in this lecture
The course – once quickly
Why do we care about verification?
What is a verification engineer?
What we’ll learn
Resources
Notes: The format of the course is the coronavirus version!

## Slide 55: Grading
Grade Formula
  Programming Assignments ≈65%
  Quizzes ≈ 35%
No tests
May (or may not) be a final project

## Slide 56: Late Assignments + Academic Integrity
10% grade reduction per day
Copying even small portions of assignments from other students or open-source projects and submitting them as your own will be a violation of academic integrity. Sharing code with other students would also be considered an offense.
The best way to ensure that your code is your own is to only have high level discussions with other students and never share a line of code.

## Slide 57: Resources
“System Verilog for Verification” by Chris Spear (2nd Ed 2008)
  free online at Tisch
  More detail on some of the topics we cover here
  Reasonably good general overview

## Slide 58: Resources
IEEE Standard for SystemVerilog
  Just type that into JumboSearch, then download the pdf (free online at Tisch)
  IEEE standard 1800-2017
  2017 version of the standard (previous was 2012)
  1300-page definitive standard on SystemVerilog
  Surprisingly easy to navigate and read (well-organized chapters)

## Slide 59: Resources
http://www.sunburst-design.com
  A SV training company
  http://www.sunburst-design.com/papers/ is a very nice collection of the papers they’ve written
  many of them are tutorial papers or “why you should code this way” papers
  but their target is working professionals in the field

## Slide 60: Resources
Comprehensive Functional Verification: The Complete Industry Cycle (Systems on Silicon, Bruce Wile, 2005
  Not available at Tisch
  $60 on Amazon/Kindle
  Encyclopedic information on verification (600+ pages)

## Slide 61: That’s all there is
That’s all there is to the course
  except, well, all of the actual details
Questions?