## Slide 1: Verification
Spring 2021
Tufts University
Instructors: Joel Grodstein, Scott Taylor
joel.grodstein@tufts.edu
staylo20@tufts.edu
Understanding the Design
Notes: This lecture covers the analysis of a hardware design– how do you determine the potential “weaknesses” of a design and know what aspects need to be verified?

## Slide 2: What’s in this lecture
Design specifications
Visualizing/analyzing the design
Typical problem areas to consider
Notes: Overall, the process of analysis consists of:
Read any/all documentation available
Internalize the design and understand its intent
Capture areas of concern and areas where there are traditionally issues
This will form the basis for your Test Plan!

## Slide 3: What are Design Specifications?
When an architect/micro-architect creates a design, there is usually a specification associated with it. There can even be many levels of documentation pertaining to a single block of logic:
  Chip-level (SOC) specifications
    Describes implementation guidelines for features that must be implemented consistently across all blocks within a design
      Power management, reset, clocks, security, RAS (error handling), test/debug hooks, etc.
  Architectural/Feature Specification
    Describes at a high level the intent of the logic, without paying attention to implementation-dependent details.
  Micro-Architectural Specification
    Describes the low level details of the logic such as pipelines, bypasses, power saving features
Notes: SOC-level specs
  These are usually written for “global” features that affect many different functional blocks, where each block has a specific set of sub-features to implement in a way that is consistent with other blocks
    All blocks must implement support for power management states
    All blocks must have a common idea of clocking, clock distribution, expected frequency ranges, clock gating for low-power design, etc
    All blocks must implement certain security restrictions to prevent hardware-based attacks
    All blocks must have consistent error handling mechanisms for reporting to a centralized error handling facility
    All blocks must support certain testability and debuggability features
Architectural Specs
  These define the design INTENT at a high level.
    A cache controller arch spec might have information on expected latencies, bandwidth, total capacity, cache coherency protocols (MESI, MESIF, etc), error protection (ECC, parity)
    A branch prediction unit spec might list the specific algorithms (local, global, hysteresis), branch mispredict mechanisms/penalties, storage array sizes
    A floating point unit spec might list the required opcodes, vector calculation requirements, register file architecture and general pipeline, number of execution units, etc.
Micro-architectural Specs
  Description of how a unit is implemented to meet the requirements of the arch spec
  These define the design IMPLEMENTATION at a low level
    Pipelining design to meet timing, including logic duplication, pipeline bypasses, feature enable/disables
    Power saving features such as clock gating
    Individual configuration/control registers
    Exact behaviors under reset conditions, error conditions, low power entry/exit, etc
    Performance features
    Bypasses and performance tweaks to meat

## Slide 4: READ the Design Specs!!
A verification engineer needs to understand the block even better than the original designer!
  How else can you find the bugs that the designer didn’t consider??
Other designers will read the spec (especially around interface behavior). If the spec is incorrect (or inadequate), then neighboring logic may not interact properly with your block
The design spec could be incomplete
  Perhaps it doesn’t cover what happens for a specific scenario you thought of
  Perhaps there’s not enough info in the spec to define what the proper response should be
Reading the spec helps us determine where the design weaknesses may be hiding
  Unclear specs often result in bugs
When there is a mismatch between design and spec… which is wrong?
Notes:       The role of the verification engineer is to try and out-think the designer!
      Where might the designer have made a mistake?
      What kind of mistake might it be?
      How might I find that mistake if it’s present?
      Incomplete specs lead to ambiguity, confusion, misunderstanding, and bugs
      What is the data returned if the transaction had an error? How does downstream logic handle that bogus data?
        Did you remember to generate good ECC/Parity for that bogus data that is returned?
      Should a data access in a mispredicted branch still be counted by the performance counters as an access?
      When a mode transitions from “off” to “on” should it take affect in the SAME CYCLE? Or on the NEXT CYCLE?

## Slide 5: Intent versus Implementation
The specs define how the designer INTENDS the block to work
  Of course, there will be mistakes (bugs) that we need to uncover. That is the job of the verification engineer!!
Architecturally, there could be bugs in the intent itself
  Cache spec says 3 cycle latency, but the product performance requirements really call for a 2-cycle cache access to meet product goals
  Security spec didn’t properly specify to protect a critical register, allowing a non-authorized user to modify kernel state
  The spec could be stale, and the implementation might be the more current “correct” behavior
Micro-architecturally, there could be bugs in the implementation
  The high-level spec is correct, but some pipeline bypasses in the design don’t handle an abort case, leading to corruption of a downstream stage of logic
  There’s a one-cycle window where the design should ungate the clocks, but fails to do so (resulting in the data for that cycle being lost)
Notes: It is important to note that there are really two types of verification:
Intent verification
  This is hard to verify without understanding the larger design! A single block might be self-consistent but incompatible with the assumptions of other blocks
    This is often an interface issue, where the sender and the receiver have different unstated assumptions
      Metric vs imperial
      Active-high vs active-low logic signalling
      Off-by-one errors (When you say “two transactions” do you mean 1,2? Or do you mean 0,1,2?)
  Sometimes there is no explicit specification of this level of behavior, and you have to figure it out on your own
Implementation verification
  Given a spec of the low-level behavior, does the design exactly implement that spec?
  This is the typical definition of “Verification” but it is really not the complete task. You might correctly verify that the design block does what the spec states, but it may still be incorrect in the larger design.

## Slide 6: How to understand the design
Read the spec.
Read it again.
  The second time, you’ve encountered all the document and may catch new things
Draw pictures!
  Pipeline diagrams
  Signal waveform diagrams and triggers
  Abstract the design into state machines
Ask questions of the designer. Have “whiteboard drawing” sessions to go over key aspects of the design.
Constantly think of the “traditional problem areas” (to be covered later in this lecture) to expose possible issues

## Slide 7: What’s in this lecture
Design specifications
Visualizing/analyzing the design
Typical problem areas to consider
Notes: Overall, the process of analysis consists of:
Read any/all documentation available
Internalize the design and understand its intent
Capture areas of concern and areas where there are traditionally issues
This will form the basis for your Test Plan!

## Slide 8: Pipeline Diagrams
Good for seeing how pipeline stages interact
Bypasses and other logic are more easily understood
T=0 | IFetch | Decode | Exe | Mem | RegWB |  |  | 
T=1 |  | IF | ID | EX | MEM | WB |  | 
T=2 |  |  | IF | ID | EX | MEM | WB | 
T=3 |  |  |  | IF | ID | EX | MEM | WB

## Slide 9: Waveform Diagrams
Draw the sequence of signal transitions
See if it makes sense.
Use it for writing checkers later.
A
B
C
D

## Slide 10: Create State Machines
Some logic can be abstracted as a (finite) state machine (FSM) even if it’s not implemented that way in the design
This can be good for understanding the design, or for creating higher level checkers
Transaction Received
Process Request
Normal Response
Error Response
Idle

## Slide 11: What’s in this lecture
Design specifications
Visualizing/analyzing the design
Typical problem areas to consider
Notes: Overall, the process of analysis consists of:
Read any/all documentation available
Internalize the design and understand its intent
Capture areas of concern and areas where there are traditionally issues
This will form the basis for your Test Plan!

## Slide 12: Where can the design go wrong?
Almost anywhere!
  Basic functionality
  Error conditions
  Power Management
  Security
  Performance features
The trick is to analyze the design with these (and other) areas in mind and see if the implementation handles all the cases…

## Slide 13: Weasel Words
“Weasel” words avoid specifying a concrete implementation and can be interpreted in different ways by different people.
Weasel Word | Example | Issue | Possible improvement
Should, Could | The response should happen within 3 cycles | Just because it should, doesn’t mean it DOES. Did this get implemented? And does it include the 3rd cycle or not? | The response must be returned between 0 and 2 cycles, inclusive.
Ideally | Ideally, the cache state should transition to “invalid” | Well, did we implement the ideal or not? | The cache state will transition to “invalid” except for the following 2 conditions:
May/Might/possibly | The cache may return data in the ‘shared’ state | Is it optional or not? | The design can optionally
Etc. | 32 bit, 64 bit, etc. | Leaves interpretation of options to the reader. Is 128 an option? | Be explicit in the list of allowed items
Need to | We need to check that the response ID matches the request ID | Unclear whether it was actually done or not | The response ID is checked against the request ID for all valid transactions

## Slide 14: Clever Tricks
Quite often, designers will implement non-obvious logic to solve a problem related to performance, timing, power, etc.
Sometimes the designer has implemented the logic in a very complicated way
  This may be due to constraints (timing, area, performance)… or it may just be a bad design choice!
Complicated logic often overlooks subtle exception conditions or unusual events
Examples
  Clock gating doesn’t re-enable the clocks on the first cycle under certain conditions
  Bypasses added to get some extra performance don’t work when the address is the same two cycles in a row
  Duplicated logic doesn’t get the same timing of all control signals, so can behave differently… but only sometimes

## Slide 15: Simultaneous Events
Designers often miss cases where two things happen at the same time…
  Read and write in same cycle… should the read get the old data, or the new data?
  Pipeline abort in the same cycle that the data is to be committed
  Reset arrives at the same time that a credit is being returned. Will the receiving logic see a credit overflow since reset will return credits to max value?
  Clocks are ungated the same cycle that a new request is coming in
  OR, clocks are gated in the same cycle that a response is to be sent

## Slide 16: Unintended Corner Cases
Different combinations of interrupts, error conditions, requests, and responses
Garbage command encoding arrives, or a valid command but with data containing bad ECC
Which control registers can change while transactions are in flight? Which control registers can only change when the unit is idle? Which control registers/modes can only change at boot time?
Resets can happen at any time. Can the design handle that cleanly?

## Slide 17: Operating Modes
Sometimes a design will have multiple customers who want to use the chip differently.
You might want to amortize costs by making one chip that serves Multiple uses. This is a “mode” of operation
Modes you may have encountered:
  Big-Endian vs Little-Endian
  32-bit data vs 64-bit data
  Number of physical address bits: 32/39/43/45/49/54/56
  MESI vs MESIF protocol support
  What others have you seen?

## Slide 18: Modes explode the state space
You have to test BOTH modes of operation– that’s twice the verification, plus overhead to support both
What happens if you can independently control Address size and Data size?
  [32 vs 64] x [32, 64] is 4x the work!
There can be many modes, so the cross-product space can be HUGE

## Slide 19: Defeatures
What happens if a feature doesn’t work in silicon??
  Fire the team?
  Respin the chip (at $40M+ for new masks, plus engineering effort, plus a delay of 2 months)?
  It’s like peeling an onion… do you have to wait for the fix to find the next problem (peeling one layer deeper in the onion)?
Or…
  do you provide a method to turn the feature off for now and see how much more you can learn before doing a respin?
  That’s a defeature!

## Slide 20: Defeature tradeoffs
You can add defeatures for risky features that don’t affect the overall product functionality too much. Choosing those is an exercise in compromise and negotiation
  Single-issue mode vs multiple issue mode
  Disable the first-level data cache
  Disable ECC checks
  Turn off hardware prefetching
  Turn off speculative execution
Hey, those sound an awful lot like modes!!
  The disables above just added 2^5=32 mode combinations to support/test…!

## Slide 21: Defeatures and Modes
Some Additional features can be disabled (defeatured) via a control register
  Examples:
    Turn off branch prediction
    Turn off prefetchers
    Reduce cache size
  Will these work in isolation? In combination with each other?
  Does the whole design work if a particular feature is disabled? Or, do other units have implicit assumptions about a feature being always enabled?

## Slide 22: Power and Clocks
Power management events can cause nonstandard flows
  Operating System requests a power-down, but we have outstanding transactions that haven’t been completed yet
  Power state exit must restore certain states that existed prior to the entry into the power state. Did we get all those bits saved/restored?
Clocks can dynamically start and stop to save power
  What happens when a cache snoop is requested but the unit’s clocks are gated?

## Slide 23: Livelock/Deadlock
Memory coherency protocols often have rigid requirements on making “forward progress”
If these are violated in the design, two parts of the chip can each be waiting for the other to respond before they can continue (DEADLOCK).
In other cases, the two units can each be making forward progress but their actions invalidate the state of the other unit, forcing it to retry its transaction repeatedly. Neither can make progress (LIVELOCK)

## Slide 24: Recap
We need to understand the design in order to reason about it and identify areas where it may be deficient
We need to think “outside the box” to come up with unusual cases or operating conditions that the designer might not have thought of
It can be helpful to visualize the design in different/multiple ways and think of it at a different level of abstraction
Consider the INTENT of the design as well as the IMPLEMENTATION

## Slide 25: Discussion Section Topics

## Slide 26: Brainstorm
Why might a performance-only feature (e.g., branch prediction) be hard to verify? (We’ll talk about this more later, too – in the Correctness lecture)

## Slide 27: Brainstorm
How would you improve the following spec for a CPU?
  The CPU should have 5 pipe stages. (Bob – should we make it six?)
  It must support full bypassing
  Branches resolve in EX and predict accordingly

## Slide 28: Brainstorm topics
Think of the most awful (unclear, buggy, whatever) homework instruction you’ve been given, or the worst spec you’ve been given for a lab
  What is it? 
  What kind of questions did you have to ask your classmates or professor to understand what to do?
  How many times did you think you were on the right track for your homework, but ended up having to rework the problem 10 times to get it right… or at least “more right” than when you started?
  This kind of ambiguity is what results in bugs!