## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
joel.grodstein@tufts.edu
staylo20@tufts.edu
Verification Concepts Overview

## Slide 2: The Big Picture
Learn the design by reading specs, talking to the designer, etc.
Define a plan for completely testing the design (the “Test Plan”). This informs all the remaining steps in the process!
Create a testbench that implements the “hooks” for controlling the design and observing its behavior
Create stimulus that drives the DUT and causes interesting behavior
Create checkers that look at the observed behavior to determine if it is behaving properly
Create coverage to confirm that you are fully exercising the design
Iterate until you have fully verified the design
Notes: There is a chicken and egg problem with teaching the material in this order:
In order to write a good test plan, you need to have some familiarity with the concepts of testbenches, stimulus, checkers, and coverage… otherwise you don’t know what you can/can’t do within the test plan
This lecture will cover the very basics of each of the concepts; enough to allow you to create a first draft of a test plan. During the term, we’ll cover all the concepts in greater detail, and then circle back around to doing the whole process on a simplified design so that you can see how the whole process works.
DUT = Device Under Test

## Slide 3: Agenda
Controllability and Observability
Testbenches
Stimulus
Checking
Coverage

## Slide 4: Brainstorm: Controlling and observing
Given the circuit below, how would you set up and time the inputs so that you
  set the node test to 1
  test if it indeed was set correctly by looking only at out2 (a cycle later)
Assume that all flops clock from the same clock
D Q
D Q
D Q
D Q
D Q
D Q
D Q
test
a0
b0
c0
d0
e0
a1
b1
c1
d1
e1
bc1
de1
test2
de2
out2

## Slide 5: What is Controllability?
In order to test a design, you must be able to control it
“Control” means the ability to manipulate the design’s inputs to cause the Design Under Test (DUT) to do what you want
In verification, the goal is to fully exercise ALL of the logic in the DUT in some meaningful way (not just the final external outputs)
  “If you haven’t tested it, it’s broken”
Exercising the logic is easy for simple combinatorial logic, but complex sequential logic requires varying the stimulus over time to get the internal state to the desired endpoint.
Modern processors are so complicated that it is virtually impossible to verify them by only looking at the chip’s primary inputs and outputs
Notes: “if you haven’t tested it, it’s broken” is the verification equivalent of Murphy’s Law.
It turns out that controlling complex designs is extremely difficult. They’re just too big to manage purely from the external pins. More on that later in this lecture.
Just because the primary inputs have been exercised and the primary outputs are correct, doesn’t mean the overall design is correct!
Example: if you have a cache miss (but it should have hit), the external pins would still behave in a completely legal manner (generating the external memory request), but internally the cache controller itself is flawed.
Example: Your design works perfectly fine unless all the data bits on the bus are zero for more than three cycles in a row. Unless you actually caused that case, you wouldn’t know there was a problem.

## Slide 6: Controllability examples
Combinatorial:
  A must be true in order to have B (or C) propagate to D
  “Path sensitization”
  D might be something deep in the middle of the design…
Sequential
  State Machine must be in REQ state in order to send CMD
A
B
C
D
IDLE
REQUEST
WAIT
RESPONSE
CMD = RD
Until ACK=1
DATA=0xABCD
Wait for REQ
Notes: Combinatorial:
If your stimulus never actually causes A to go high, then it doesn’t matter whether B and C are correct because they are never consumed.
This is a core tenet of “fault grading” for manufacturing coverage, and Automatic Test Pattern Generation (ATPG) concepts can analyze the design to shift appropriate data into the design’s flops to cover the individual cases in a limited number of cycles.
But, that’s using manufacturing/test techniques that are not valid for normal functional operation. In normal modes of operation, you lack that level of controllability and have to work upstream in the logic cone to get what you need.
Therefore, full verification ideally needs to ensure that every signal in the design is actually consumed. You might even want to cover different combinations of signal values.

## Slide 7: Types of Controllability
Direct control of individual primary input/output pins of the DUT
  Drive reset=1 for 3 cycles
  Drive a 1.67GHz clock input for the duration of the simulation
Bus Functional Model
  Mimics a higher abstraction such as a bus protocol, I/O device, or the behavior of another piece of the design
    PCIE
    Main Memory
    Interrupt controller
Jamming/Forcing internal design nodes to override RTL behavior
  Perhaps to test a bug fix
  Perhaps to inject errors (Parity, DMA, bus corruption, etc)
Notes: We’ll cover BFMs in much greater detail in a later lecture. For now, just think of it as a way to intelligently control things at the signal level, using input that is more sensible/abstract (like saying “Read” instead of wiggling the command and control signals across multiple clock cycles)
BFMs are also called “Transactors”, and sometimes overlap with “Drivers” and “Monitors”. We’ll talk about those later.

## Slide 8: Brainstorm: Cache preload
One feature that most CPU testbenches support is cache preload – i.e., the ability for the verification environment to directly stuff binary instructions into a CPU’s ICache
  why might this be so important?

## Slide 9: What is Observability?
Once you have caused the DUT to do something “interesting”, how do you know what it actually did?
To “observe” is to have some part of your simulation environment that wraps around the DUT (the “Testbench”) able to see key behaviors of the DUT. This is typically called a “monitor”.
“If you can’t see it, it’s broken”
Note: Observability is only the ability to SEE the results.
  It doesn’t say whether those results are CORRECT! That’s a “Checker” and is different from a “monitor”.
  Observability “feeds” the checkers, and it’s sometimes hard to separate the two.

## Slide 10: Observability examples
Core does a write to a cache line. How do you know whether it got there correctly?
  Something has to either look at the data, or depend on it for proper operation
You’re trying to cause a branch mispredict to see if instructions executing in the shadow of the branch inadvertently update architectural state. How do you know if you got the intended branch misprediction?
How do you know if an error condition occurred?
How do you tell if a bus transaction completed successfully?
Did the frame buffer for the current screen redraw contain the correct set of image data?
Notes: Again, we’re mixing “observe the results” and “are the results correct” on this slide. Observability gets/monitors the data. Later in the lecture we’ll cover the correctness checking of those results.
Observability is fundamentally at the signal level, but we can build abstractions via “monitors” that can pull together data into a more meaningful “transaction”. This will be covered in more detail in a later lecture.
Observed signals can actually feed MULTIPLE checkers (for instance, a valid bit on a request might be used for triggering a check on whether a response was later generated. That same valid bit might also be used at the interface level to check whether the request payload (cmd, address, etc) associated with the valid bit is indeed legal.

## Slide 11: Types of Observability
Direct
  Have your testbench look directly at a signal or signals. These could be the primary outputs, or could be a purely internal signal
Indirect
  Ensure (via controllability!) that the desired state causes the design to behave differently in the “good” and “bad” cases, and then look at that downstream behavior to infer whether your target signal did the right thing
For the “Did we write the cache line” example, you could
  Read the data back and branch to pass/fail based on the result (indirect)
  Use the testbench to poke directly into the cache signals to see if the data is present (direct)
Notes: Again, Monitors can be used to take multiple signals (at the same time, or across multiple cycles) and abstract them into a “transaction” that a checker can more easily consume. We’ll cover this in great detail in a later lecture.
Direct checking can be useful, but is more intrusive. It can be hard to know exactly WHEN to look at a signal to see if it was correct.
Indirect doesn’t rely on exact timing, but can be more difficult to set up the proper conditions.
It’s a tradeoff.

## Slide 12: Brainstorm: Observability
In the previous example of “do a program read of the data to see if the data was a hit”….
  Why won’t this work??
  What might you be able to do/enhance to resolve the issue?
Notes: Discuss: What might go wrong with the indirect method of verifying “Did we write the cache line”?
It might not have written, and you might have read the value from memory… which would look like a hit,
How might you distinguish between a hit and a miss?
  You could count cycles. A hit will take less time than a miss!
  You could fall back on direct testbench poking
  You could have a monitor that detects hit vs miss and a checker that you arm to fire if you get a miss during the critical segment
  There are other options too

## Slide 13: Breaking down the design
A full chip is generally too complicated to test as a single monolithic unit
  Too slow to simulate
  Too complicated to control the deep internals
  Too hard to force every signal behavior to be visible at the external pins to determine pass/fail
Therefore, we typically “divide and conquer” the design by breaking it into manageable pieces (units)
Each piece can be individually tested, and then more limited testing done at the full chip level to exercise interactions BETWEEN the pieces
There can be MULTIPLE layers of pieces that all build up to the full design!
  Multiple units can be combined into a larger integrated unit, and so on
Notes: How slow is slow?
A single unit might be 1000 cycles/sec
A collection of units (like a core) might be 100 cycles/sec
A CPU might be 10 cycles/sec
A full SOC might be 1 cycle/sec
Imagine trying to cause the pins of an SOC to behave differently based on whether the GPU rendered a specific triangle or not!
Imagine trying to get a specific transaction between the CPU and the GPU purely from a user-level program.

## Slide 14: SOC
Primary inputs might be
  Clock oscillator
  Reset
  DRAM
  PCI
  HDMI
How do you fully test CPU, GPU, etc using only those interfaces??
Memory
Controller
CPU
GPU
PCIE
Display
Coherency Engine
Camera
Codec
Misc

## Slide 15: CPU
Here, we have some more controllability and interfaces that are closer to the logic.
We don’t have to worry about configuring units that aren’t present (simplifies our modeling)
However, still difficult to control the behavior of a single unit within the CPU
Exe Cores
Caches
Interrupt CTL
Local Coherency CTL
Exe Cores

## Slide 16: Core
Smaller amount of logic to control; better control over a single core than a whole CPU containing multiple cores and a shared cache
Fetch/Decode
Integer
Floating Pt
LD/ST unit
Reg Files

## Slide 17: Integer Unit
Here we have direct control over individual opcodes and register values
Small amount of logic means very fast simulations
Easy to control and observe
Integer Exe

## Slide 18: Controlling and observing
Consider the examples in slides 12-15. Assume that
  in slide 12, you are trying to test the GPU
  in each of slides 13-15, you are trying to test the integer unit of one core
For each of these four cases
  what would you drive to control the test?
  how would you observe the results?

## Slide 19: Benefits and disadvantages of unit vs integration levels
Unit-level testing
  Pros
    Easy to control
    Faster
    Easy for one person to hold it all in their head
  Cons
    Many assumptions on how the “other” units behave
    Must model those other unit behaviors
    Can’t fully test interactions
Integration-level testing
  Pros
    More of the logic is “real”
    Can test interactions between internal units
  Cons
    Harder to control behaviors between units
    Slower
    Usually involves multiple people due to size of design

## Slide 20: Agenda
Controllability and Observability
Testbenches
Stimulus
Checking
Coverage

## Slide 21: Testbenches
Depending on what level of unit/integration you choose, you need to create a testbench that will drive the primary inputs of that DUT and observe the outputs. This is called the “testbench”.
A testbench is the set of components that implement your stimulus, checking, and coverage.
You don’t want too MANY levels of units/hierarchies, as that is more work to create unique components for each layer
But you don’t want too FEW levels, either, as that makes it harder to fully test each one. It’s a balance!
Ideally you want to re-use components between layers that share a functional unit or interface (don’t re-invent the wheel!)

## Slide 22: Example unit testbench
DUT
(single CPU Core)
Checking
Stimulus
Coverage
Clock Driver
Reset Driver
Interrupt driver
Memory
Test and Debug interface driver
Quiescence
Other
Coherency
Reset Rules
Power Mgmt
Mem/Cache preloader
End of Sim detection
Control Register I/F
Performance
All Opcodes
Clock freq
Mem Req types
Mem Rsp types
CTL Reg modes
Notes: For a different unit, some of the components might be the same (or similar) but others would be completely different.
For a different level of integration, some of these components could be reused (e.g. the memory preloader, or the quiescence checks) while others would not (like the interrupt driver, which might be real RTL at a higher level of integration… or the coherency checks, which might be very different at a higher integration)
Note that not all “stimulus” is drive-only.
Consider main memory, which need to be read and written. You load stimulus into it, but it is technically more of the “other” category and would probably be merged with the mem/cache preloader to create a single reusable “memory” component that all testbenches share.

## Slide 23: Brainstorm: Testbenches
Given the previous slide, what might change if the DUT was changed to be:
  The full SOC?
  Just an integer unit?
  Just a cache and its control logic?

## Slide 24: Agenda
Controllability and Observability
Testbenches
Stimulus
Checking
Coverage

## Slide 25: Stimulus
Stimulus is the method by which you provide controllability
Stimulus can take many forms, depending on the DUT. It consists of one or more items:
  A “program” (instruction stream) or sequence of commands
  Memory contents (data stream) that are to be consumed or operated upon
  “Side instructions” to a BFM (perhaps to cause interrupts at a specific time)
  Direct forces of primary inputs (clocks, resets) at a specific moment
  Direct forces of internal nodes (configuration registers, parity bits, driving “X” values)
When you plan your verification, you need to determine what kinds of stimulus are needed (and where) in order to fully explore your design!

## Slide 26: Types of stimulus
Hard coded (“Directed testing”)
  E.g. text file with a list of specific transactions to send and at what times
Random
  Purely random is rarely used (think of a program with completely random bits!)
  Pseudo-random (or “Directed random”, or “Constrained random”) is prevalent
    Choose 40% reads and 60% writes for the command field
Stimulus can be independent of DUT state, or can be reactive
  Independent: send a series of random values for the texture map
  Reactive: If core11 is within three cycles of entering a powerdown state, send a snoop request 5% of the time
    Discuss: Why is that specific timing relationship interesting? Think back to previous lecture on design interactions!

## Slide 27: Agenda
Controllability and Observability
Testbenches
Stimulus
Checking
Coverage

## Slide 28: Checking
Checking is one of the forms of observability
Checkers implement a set of RULES that the design must obey.
Checkers define the expected behavior of some part of the design
  Legal and illegal outputs
Checkers usually consume internal RTL state or primary outputs
Checkers need to know the “right answer” somehow (more on this in a future lecture!)
Checkers need to know when it’s VALID to do the check
  Is it true for all times? Or is it only true under certain conditions?
Checks can be narrow (single signal) or broad (overall behavior of an entire functional unit)

## Slide 29: Types of Checking
Design assertions within the design RTL for simple relationships
  Illegal encodings
Testbench objects (Checkers) that look at a specific signal, interface, or functional unit, and confirm the proper behavior is occurring
  Checkers can look for correct values at a point in time
    Data should be 0x1234 for the current request
  Checkers can look for consistency between two different signals
    If valid=1, then cmd must be one of 5 valid encodings

## Slide 30: Types of Checking
Checkers can look for illegal behaviors
  No invalid opcodes
  No parity errors are expected in this test (but might be expected for a DIFFERENT test!)
  Clock must always have a 50% duty cycle (No glitches or “runt pulses”)
Checkers can look for more abstract expected behaviors
  A new cache request to index A should cause an eviction of any dirty data in index A
  A power management request to the C7 state should ultimately result in removal of power to the requesting core
  At the end of a test, all queues and FIFOs must be empty and all credits at their max values (“quiescence”)
Checkers can look for the LACK of a behavior
  Didn’t detect error
  Didn’t respond in the allowed timeframe
Notes: Power Management primer:
C0: Active
C1: Clocks Gated
C3: Power reduced to “retention” levels. Operation impossible, but state is maintained
C7: Power is completed gated/turned off

## Slide 31: Where do we get ideas for checker rules?
General analysis/knowledge of the design will reveal some obvious rules
  FIFOs should process entries in a specific defined order
  A block shouldn’t produce any transactions if its clock is supposed to be gated
The various design specifications will provide others
  PCIE protocol rules (architectural spec)
  Credit/debit rules on number of outstanding requests allowed (microarchitectural spec)
  Memory Coherency rules (MESI, etc)
As you write the test plan for your block, you capture all these rules and then decide HOW they will be checked

## Slide 32: Agenda
Controllability and Observability
Testbenches
Stimulus
Checking
Coverage

## Slide 33: Coverage
“Coverage” is another form of observability
Coverage is a way of determining if certain events have or haven’t occurred
  These could be individual events, or sequences of events over time
Coverage gives an idea of how good your stimulus of the design is.
Coverage can tell you when there are holes in your verification plan
Coverage can be measured for a single testcase, but is more often aggregated across many simulations to get a better idea of overall design and testcase quality

## Slide 34: Types of Coverage
RTL coverage
  Line coverage (tells whether each line of RTL has been executed)
  Toggle coverage (tells whether each signal in the RTL has had a 0->1 transition as well as a 1->0 transition
  Condition coverage (tells whether conditional logic has executed both sides of the condition)
Functional coverage
  More abstract; implies some design knowledge
  All possible (legal) values for an encoding
  Sequences of events (Back to back transactions with the same address)
  Finite State Machine (FSM) coverage
    Did we enter all legal states? Did we transition via all legal arcs?