## Slide 1
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
joel.grodstein@tufts.edu
staylo20@tufts.edu
Test Plans

## Slide 2: What’s in this lecture
Goals of a Test Plan
Granularity of a Test Plan
Parts of a Test Plan
Test Plans IRL
Putting it all together

## Slide 3: Why do we need Test Plans?
Designs are too complicated to “wing it”.
Verification is a systematic method for achieving confidence in the design quality.
  Emphasis on SYSTEMATIC!
Careful analysis and planning, by itself, can find bugs
By specifying EVERYTHING we intend to test, others can review the document and point out areas we have missed
We need a complete list of tasks and activities so we can scope the effort and timeframe
  How many people do we need, and for how long?
Notes: Just the act of getting lots of people in a room (from both design and verif) talking about things finds lots of design bugs and test holes
Get it all out there and occasionally/often look stupid – it may bit a bit embarrassing, but it’s a lot better than finding issues too late.
The last bullet may sound like an afterthought, but it’s really one of the primary motivators for having a good plan up front… otherwise your management won’t staff it and you’ll be overloaded, overwhelmed, overworked, and over-stressed! I.e., this is where you negotiate people, schedule and feature reduction with management.

## Slide 4: Test Plan Goals
Specify ALL the planned work for an area
  Environment, Testbench, Stimulus, Checking, Coverage, etc
Divide into reasonably sized concrete tasks with effort analysis
  More on this later. This is very hard!
Define what THIS plan is covering, and what OTHER plans are assumed/guaranteed to be covering
  No “underlaps”, and only sensible “overlaps”
Define the “staging order” of task execution
Track what parts are completed, and which aren’t.
Notes: This is where you make sure your plans don’t include staying up all night before the work is due 
Note the “PLANNED” work… you’ll almost always find more work than what you planned as you better understand the design. And engineers suck at planning! Most good engineers tend to overestimate our own abilities – and most managers like to hold us to those estimates 
Underlaps: I thought you were doing that; no, I thought you were doing it! Overlaps are a fine balance – they pay us to be paranoid, but overlaps cost money

## Slide 5: Test Plan NON-Goals
A test plan is not…
The only measurement of “doneness”, or even “the total work”.
  There are other tools and analysis methods that complement this.
A static document.
  The test plan will evolve over time as all parties better understand the design and its weaknesses
Foolproof.
  A plan is only as good as the things you THINK about adding to it.
  “If you didn’t think about it, it’s probably broken”
Notes: As you find more bugs and/or miss your coverage targets, you’ll know where to put more people and do more testing work -- the test plan won’t be static.

## Slide 6: Test Plan Terminology
Test Plan
  A document that defines a set of tasks that verify all aspects of some portion of the design
Task
  A specific action that has a deliverable, an effort, and a deadline. There are many other attributes of a task that can vary based on the type of task.
Test
  A specific set of stimulus (with associated correctness checking) designed to accomplish a specific action/response in the design.
Notes: Other attributes of a task: has an owner and a priority
Example task: “write test XYZ.” Or “write the tests needed to get 95% coverage of this unit.” One test may cover many tasks, or you may need many tests for one task.

## Slide 7: What’s in this lecture
Goals of a Test Plan
Granularity of a Test Plan
Parts of a Test Plan
Test Plans IRL
Putting it all together

## Slide 8: What does a test plan cover, anyway?
There’s not just ONE test plan for a chip!
We divide the effort into several overlapping areas
  Unit-level plans
  Feature-level plans
  Integration-level plans
Notes: Review question: how do you decide what gets covered at unit level and what gets covered at a higher level?

## Slide 9: Unit Level Plans
Usually covers a specific “geographic area” of the chip
  Functional unit granularity
    Integer unit
    Cache controller
    PCIE controller
    Shader unit
  Sometimes we overload or subdivide this to cover a specific environment for the unit
    RTL-level simulation plan
    Gate-level simulation plan
    Emulation plan
    Silicon plan
These usually get executed in this order over time

## Slide 10: Feature-level Plans
Some features/flows can’t be mapped to a single geographic location or design hierarchy because they span many/all units
  Security
  Error handling (RAS)
  Clocks
  Reset
  Memory Coherency

## Slide 11: Feature-level Plans
Some features require specialized plans that concentrate on the feature or flow rather than the underlying logic
  “End-to-end checkers”
  Ensure consistent handling of the feature/flow across units
Feature-level plans often don’t have their own testbench/environment

## Slide 12: Feature-level Plans
Feature-level plans will overlap with unit and integration plans!
  Difficult to determine/negotiate which tasks go into which plan
Often, Feature-level plans are a “Master plan” that shows all the work related to a feature, and documents which plan will cover which piece
  Remember, we want to test things in the lowest level environment that we can!
Feature Testplan:
  Task 1 (Core plan)
  Task 2 (Interrupt plan)
  Task 3 (covered in this plan)
  Task 4 (SOC plan)
Core Testplan:
Task 1
Interrupt Testplan:
Task 2
SOC Testplan:
Task 4

## Slide 13: Integration-level Plans
Test a feature in the lowest level of model that can be used
  Don’t test instruction cache parity generator at the SOC level!
  Instead, use the smallest environment (like the execution core testbench) so you can maximize Controllability and Observability
  This makes your test plan easier to write/execute
Focus only on the features that are UNIQUE to a higher level integration
  Interactions of units
  Wrapper logic that only exists above your unit level testbenches
  End-to-end checking that passes through multiple units

## Slide 14: What about overlap?
We have limited resources (That’s management-speak for engineers)
We can’t afford to verify the same thing over and over in every testbench/integration level.
If you’ve completely verified something in a low level testbench, what’s the benefit of testing it a second time at a higher level??
However, SOME overlap is desirable
  Confirms any assumptions that the lower level environment might have made
  We are paid to be paranoid!

## Slide 15: Possible CPU Test Plan Granularity
Integer Unit
Floating-pt Unit
L2 Cache
CPU Core
Units
Integrations
Features
Cluster of cores
Full CPU
SOC
Debug Controller
Interrupt Handler
L3 Cache
CPU Cache/ mem intf
Coherency Master
RAS
Security
DFT
DFD
Clocks
Reset
Interrupts
Coherency
Other SOC Stuff

## Slide 16: What’s in this lecture
Goals of a Test Plan
Granularity of a Test Plan
Parts of a Test Plan
Test Plans IRL
Putting it all together

## Slide 17: Organizing your Test Plan
A single test plan can be very short for simple/small designs (a few pages), or extremely long for more complicated features (hundreds of pages)
  A recent CPU I worked on had 1700 total pages across all testplans, not including the rest of the SOC!
Good organization is CRITICAL to defining and executing such plans!

## Slide 18: Critical pieces of a testplan
What are your REFERENCE DOCUMENTS?
What are your ASSUMPTIONS?
What’s the overall STRATEGY?
What TESTBENCHES/environments do you need?
What unique STIMULUS do you need to create for each testbench?
What’s the CHECKING strategy?
How do you measure doneness (COVERAGE)?
For each of the above, what are the TASKS that have to be executed?

## Slide 19: Reference Documents
List the documents you read as part of understanding the design
Include the specific VERSION of the document!!
  That way you know to review things when a newer version comes out. It might change your test plan!

## Slide 20: Assumptions
What work do you believe will be covered by others?
  YOU MUST CONFIRM THIS!!!!
What design assumptions are you relying on?
What external (to you) tools do you require?
  What are your dependencies? Who do you need stuff from, and who needs stuff from you? Can you deliver?

## Slide 21: Strategy
How do you plan to approach testing this area of the chip?
This will usually involve discussion of testbench, stimulus, checking, coverage, tools, Formal Verif, Emulation, etc
What is your rationale for deciding what testbenches will be used to cover specific tasks?

## Slide 22: Testbenches
What testbenches are required to test aspects of this piece of the design? Why? Does your testplan create additional requirements for that testbench
What are your assumptions for testcase runtimes? (test length and cycles-per-second should both be considered)
  Discuss: Why is this important?
Will some components be shared across multiple environments?
  Example: ECC generator/checker

## Slide 23: Stimulus
What stimulus can you re-use from prior/existing work?
What new stimulus needs to be created from scratch for this project area?
What dependencies do you have on other teams? (and vice versa)

## Slide 24: Checking
Can you share/reuse existing checkers?
Extend/modify existing checkers?
Create entirely new checkers?
What kind of checkers will you write?
  Reference models, self-checking code, scoreboards, etc.
Will checks happen during the test, or at the end, or as a post-processing step?

## Slide 25: Coverage
How much coverage is required?
  Focused/hard-coded self-checking tests might not need much
  Purely random tests might need a lot
What kinds of coverage are needed?
  RTL code coverage?
  Verification code coverage?
  Functional coverage?
  Visual Inspection?
    (this is manual eyeball review of simulation results, or just reading the code)
    Discuss: When is “visual inspection” a good idea?
Discuss: How often does coverage need to be collected? Throughout the project, or just at the end?

## Slide 26: What’s in this lecture
Goals of a Test Plan
Granularity of a Test Plan
Parts of a Test Plan
Test Plans IRL
Putting it all together

## Slide 27: Where does the Test Plan fit in the design life-cycle?
Architecture Definition
RTL Development starts
Arch Frozen
RTL Complete
Phys Design starts
Phys Complete
Tape-out
First
Silicon
Final Spin
Profit!
Product Definition
Write Test plan
Initial Review
Execution Begins
Test
Plan
Intermediate Review
Final Review
Final
Sign-off

## Slide 28: Test Plan Dependencies
Can’t start test plan until high level architecture is defined
Can’t define the full set of tasks until low-level microarchitecture/implementation is defined and (at least partially) coded
Basic design definition drives “initial review”
Arch Freeze (no more feature changes) drives “intermediate review”
RTL Complete (== “All bugs coded!”) drives final review
Test Plan completion/sign-off gates tapeout
You can have dependencies BETWEEN test plans, too!
Notes: Dependencies between test plans can include:
Shared collateral developed by one team and given to another team
Test parts of a feature at a lower level before testing them at a higher level of integration
Resource (engineer) staffing dependencies (person moves from area to area over time)

## Slide 29: Scoping tasks (Effort Estimation)
Determining how long it takes to execute a task is probably the hardest thing for an engineer to do.
It can’t really be taught 
Once you have experience with doing tasks for a specific job, it becomes easier to make educated guesses about duration of a task.
Sometimes you can extrapolate from a similar task that someone else has scoped.
ENGINEERS ALMOST ALWAYS UNDERESTIMATE A TASK!
  Scott’s Rule of Thumb: For an estimate of size X, the manager will ask it to be 0.5x, and the actual duration will be 2.5x.

## Slide 30: Follow the bugs!
There are a number of areas where bugs will commonly appear
  They are not usually on the “normal path of execution”
Some design areas are prone to have similar bugs every chip generation
On the other hand, some problems only exist for a single generation and we learn from our mistakes.
So, where should a verification plan focus?
  CORNER CASES!

## Slide 31: Areas to consider for bugs
Back in the “Understanding the Design” lecture, we talked about this
Consider “normal operation” as the area that will get the most attention. You still have to verify it, but it will get LOTS of cycles!
Almost everything else is the “rare cross-product”
  The bugs will usually be hiding here…

## Slide 32: Areas to consider for bugs
Basic functionality
Error conditions
Power Management
Security
Performance features
“Clever” optimizations
Simultaneous events
Unintentional interactions
Bad handling of “illegal” scenarios
Modes of operation (And interaction of modes)
Clock interactions
Notes: Clever optimizations often happen for these reasons:
Power reduction
Performance improvement (more efficient, or just faster frequency/timing)
Area reduction
Overly ambitious designer

## Slide 33: Test Plan Reviews
There are usually multiple reviews
One early, when we have the basic architecture defined
  Often this concentrates on the overall strategy since the implementation details aren’t fully defined
One mid-project, when the full RTL design is defined and spec’d
  This is when you have all the documentation you’re likely to get
  This is the main review
One at the end of the project, to confirm you actually did everything you said you’d do. “Sign-off”

## Slide 34: Test Plan Reviews
Reviews usually involve the architect, RTL designer, the team executing the testplan, and a few senior verif engineers to act as a safety net
The idea is to review where there may be:
  Identify underlaps (Gaps) or overlaps (redundant work) with other test plans
  Mistakes in assumptions
  Mistakes in testing of design intent (usually caused by miscommunication or inadequate design documentation)
  Errors in judgment on strategy, effort, etc.

## Slide 35: Test Plan Execution
The bulk of a project (70%) is the execution of the plan you have put together.
The better the quality and readability of the plan, the smoother the execution
A single test plan might have a hundred tasks that have to be scheduled across a six months or a year of time.
A full CPU might have 1000 or 1500 tasks.
WHAT ORDER DO YOU WORK ON THEM???

## Slide 36: Dependencies, Dependencies, Dependencies…
“Before you can do anything, you have to do something else first”
  Attributed to Murphy
Execution plans require a “phasing plan” alongside that defines what we do first, and what is enabled by each task
  Or conversely, what tasks can’t start until some other task has been completed
Defining this correctly can be difficult
Managers may track it, but the engineers define it
Always list your assumptions and dependencies in every test plan task

## Slide 37: When are you done? When is Tapeout?
When your plan is completed 100% and signed off
When your manager says you’re done
When the physical design is ready for tapeout
You’d like to think it’s #1… but most of the time #3 is the dominant factor!

## Slide 38: What’s in this lecture
Goals of a Test Plan
Granularity of a Test Plan
Parts of a Test Plan
Test Plans IRL
Putting it all together

## Slide 39: Putting it all together
Let’s consider a simple feature in a block, and the process of creating the test plan around that one small piece
This is a completely fictitious design example and test plan to illustrate the process…

## Slide 40: Cache system control logic
S3
Cache
S4
Address
Clk
Data

## Slide 41: Sample implementation?
S3
Cache
S4
Address
Clk
Data
S4
==?
Current cycle addr
Prev cycle addr
Notes: Note the changes from the previous slide
The data might recirculate instead of grabbing from the cache. (this makes sense if you access the same address multiple cycles in a row; it’s lower power to recirculate a latch than it is to do a full cache lookup
The decision to do this is drawn from whether the current and previous cycle addresses were the same (the comparison on the bottom latches)

## Slide 42: The spec
Section 2.5.7.6.8.7.6 of the L2 Cache Controller spec mentions this phrase that gets your attention:
“To save power, if the cache is accessed with the same address in consecutive cycles, the earlier read result is bypassed to the later read.”
Hmmmm… What could possibly go wrong with THAT??
Notes: What’s vague about this?
Brainstorm ideas about what might go wrong.

## Slide 43: Defining the Task(s)
What’s in a task?
Detailed description of what to test and how to test it
What is the test strategy? Is it a checker, or a self-contained testcase, or some coverage?
When does it have to be completed (deadline)?
How much effort (1 day? 4 months?)
What are the dependencies on task completion? (both input and output dependencies)
What’s the status of the task? (not started, Work In Progress, Blocked, Done, etc)
What’s the priority of the task? (critical, normal, nice-to-have, etc)
Who owns the task execution?

## Slide 44: Initial task description
After some email discussions with the designer to get more details, you start with this initial description:
Description: Test back-to-back transactions with the same address
  The L2 Cache controller pipeline has bypass logic between the S3 and S4 stages so that if the same address is requested in consecutive cycles, we don’t have to read the cache line twice, but can bypass the previously read value into the later stage. This saves 6mW of power because we don’t have to activate the cache itself in that cycle.
Seems simple enough. We just need to issue the same access twice in a row, right? Or… is there more to it than just that?
Notes: Back to back is definitely a stimulus requirement. Sure, doing that makes sense. How often, though? And how do we check this bypass behavior? And how do we know we exercised it?

## Slide 45: The simple tasks
TASK 1
  We will constrain the random address generator to generate the same address in consecutive cycles 10% of the time (2 days effort; owner=Tim)
Task 2
  The existing cache data checker uses an abstract non-pipelined model of the cache and will read the data each time. This provides the necessary check that the correct data is always generated at the output of the unit. (0 days effort)
Task 3
  We require functional coverage to confirm we have had back-to-back accesses with the same address. We will look at the incoming address port for this (1.5 days effort; owner = Rana)

## Slide 46: Thinking of what might go wrong
So, what could go wrong here? What other things might affect that bypass in the pipeline? After thinking about it (and asking more questions), you realize it’s not as simple as was mentioned in the spec.

## Slide 47: Sample implementation?
S3
Cache
S4
Address
Clk
Data
S4
==?
Current cycle addr
Prev cycle addr

## Slide 48: What about Write operations?
What about simultaneous reads/writes??
What happens with newly written data to the same address?
  If there is a write to the cache line in the same S3 cycle that it is read, the write-data must be bypassed to both the S3 and S4 read stages.
  If there is a write to the cache line in the same S4 cycle that it is read, the write data must be bypassed from the write data and not from the S3 read.
  The above statements are assuming a simultaneous RD/WR is supported by the design. Perhaps you should check with the designer on that…

## Slide 49
S3
Cache
S4
Address
Clk
Data
S4
==?
Current cycle addr
Prev cycle addr
Wr Data
Rd/Wr
S3
S3
S4
Hmmm…What’s this mux input for?
Notes: Note: The blue arrow is pointing to the red input to the mux.
It seems to IMPLY that you’re taking a single-port RAM and allowing a subset of WR + RD to the same address. It’s probably more complicated than shown, but is out of the scope of the specific test plan item we’re discussing.
However, you might want to go to the designer to confirm that this is intended behavior. Perhaps it’s another unexpected/undocumented test plan line item!

## Slide 50: More tasks
Task 4
  Test generator needs to have a mix of reads and writes to the same address, happening around the same time in the execution thread
    The existing generator doesn’t coordinate read/write traffic; it was completely random. So, we need to add a capability to the chooser to sometimes choose a recently used READ address as the WRITE address, and vice versa.
    Perhaps we can just keep a queue of the last 10 addresses, and 10% of the time reuse one of those to cover both cases?
    Tim estimates that is 3 days of additional work, so you add that as the effort for the new Task4.
Task 5
  We need additional coverage to see if we have hit the following conditions:
    Write to address A in S3, and simultaneous read of address A in both S3 and S4
    Write to Address A in S3, and read of Address A only in S4 (to ensure the bypass didn’t accidentally activate)

## Slide 51: What about unexpected events?
What might happen if there’s an ECC error in the cache line when it’s read?
  You know that the correction logic takes an extra cycle to run, so will the bypass work? Nope!
  After talking with the designer, it’s determined to be a bug and you add a test plan task to make sure the improved design will actually work

## Slide 52: Error crossproduct task Example
Task 4:
  There can be an ECC error in S3 for the read data. Test that in such cases, the controller does NOT do a bypass into S4 because the data would not yet be corrected. This requires:
    1) Ability to generate random ECC errors. This already exists in separate task 1234.
    2) Additional coverage to detect cases where we have back to back access of the same address AND the first access was an ECC error. This is an additional 1 day of effort on top of Task 3. Owner=Rana
(Note that here both items were dumped in one task; this ties them together clearly, but if a task ends up with multiple owners it can get confusing, so use this sparingly)
Notes: Open question: How should Rana feel about being given another task? Is this something she should push back on? Or accept on top of her existing workload? What are the ways Rana could react to her tech lead or manager?

## Slide 53: What else could go wrong?
Thinking about the problem, you realize that the bypass must be comparing address bits. But is it actually looking at the correct bits? All the bits?

## Slide 54: Task Example
Task 5:
  Make sure that the full range of address bits is used in the comparison, not just the index bits!
  Extend the address generator to create random transactions where the index is the same but some tag bits differ. (1 day; owner=Chin)
  Existing data checker will fire if the wrong data is ever bypassed into the later stage (no extra effort)
    Question: This assumes that the data for the different addresses different! There is a risk that the data for both reads is the same (Cache of mostly zeros, for instance)… how might you handle detecting that case?

## Slide 55: But what about the “Power Savings”?
We’ve been looking at the trees, but what about the forest?
The whole bypass was put in place to save power, right? Where’s the logic that actually causes that power reduction??
  Probably some kind of CLOCK GATING is needed on the input to the cache logic… or some other method of lowering the power during that cycle.
  What needs to be added to test that we actually activate those power savings when needed (and not when operating normally)?
  How do we measure the power to see if we got the expected savings? Is it a bug if we only got 4mW of savings instead of the spec’d 6mW?