## Slide 1: Verification
Spring 2022
Tufts University
Instructors: Joel Grodstein, Scott Taylor
Post silicon

## Slide 2: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Visibility and debug hooks
Life in post silicon
Mock debug, war stories

## Slide 3: When is Post-silicon?
When you already did:
  as much verification as you had time for on an RTL model
  you finished as much of your test plan as you could
  you didn’t prove the chip works!
  and it probably doesn’t 
  But your boss’ boss said it’s time to tape out

## Slide 4
Remember this slide?
Now the real work starts  This time, on actual silicon

## Slide 5: Cost of a bug fix
Early in design: 1 engineer week ($5K)
Late in design: 1 week tapeout slip = $2M
  or 1 week = 1% performance
Post-silicon: 1 extra tapeout ($+2 months) = $20M
Post-FRS: lose 20% of your customers = $20M/year
After substantial field volume: recalls
  1995 Pentium fix = $495M
400x
4000x
100,000x
Remember this slide?
Really really want to avoid these, and multiple 2-month delays
Notes: Assume you’re selling a GPU; 1M units/year, $100/unit. so $100M/year or $2M/week
Hard to compute the cost of a tapeout (depends on your volume, etc and how many layers it involves). Scott’s numbers are $1M/layer, or $40M for a full-layer tapeout and $20M for metal-only. I’ll use $50M since Scott’s numbers are slightly old.

## Slide 6: What’s about to hit you?
What’s the difference between theory and practice?
  In theory, there is no difference
  In practice, there is
RTL is a fast gate-level (or higher) abstraction
  Real life is transistors
  and R, C, L, asynchronous clocks, coupling, …
Simple models for DRAM, peripherals, external networks are now the real thing
Your modeling safety net is now gone
  Physics rears its ugly head
  Analog behaviors suddenly become relevant
  Some companies treat electrical debug separately
Notes: Really, this slide is more about electrical debug. But the functional verification people still have to deal with it too.
And replacing the BFMs with real DRAM is a big deal.

## Slide 7: Speed matters
Pre-silicon RTL model ≈ 10 cycles/sec
  630∙109 cycles
Real machine runs at 3 GHz = 3∙ 109 cycles/sec
Your entire pre-silicon verification effort is replicated in <4 minutes on one chip!
  Lots of cycles to turn up corner cases
  But no free lunch 

## Slide 8: The good, the bad and the ugly
Good
  tests run really fast. So you “might” find failures fast
  you’re starting with a chip that has been “mostly” debugged. Hopefully relatively few failures left!
Bad
  the “might” and “mostly” above
  very little visibility or repeatability
  fixing silicon ≠ fixing software
  these are a really big deal!

## Slide 9: The ugly
One time, several years ago, I was called into a room with management and asked not only how long was it going to take to resolve the current bug we were working on, but also, how many more bugs we were going to have before the product was able to go into production. I tried to explain that if we knew how many bugs there were and how long they would take to resolve, we wouldn’t have put them there in the first place, but my explanation was just met with a room full of blank stares.
    The crazy mixed up world of silicon debug, Doug Josephson, 2005
Notes: The point – lots of pressure.
No place left to kick the can further down the road. The buck stops here.

## Slide 10: The ugly
Such is the nature of silicon debug. To be successful, the debug engineer must be able to solve problems in areas where he has no technical expertise, drive design teams to make changes where he has no influence, and be able to predict the future. These are a few of the tasks that make the silicon debug experience so challenging and exciting.
    The crazy mixed up world of silicon debug, Doug Josephson, 2005

## Slide 11: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Visibility and debug hooks
Life in post silicon
Mock debug, war stories

## Slide 12: Tests might run really fast
Yes, the chip runs really fast
Does that mean your tests will?

## Slide 13: Overly Simplified Testbench
RTL
DUT
Checking
Stimulus
Coverage
Clock Driver
Reset Driver
Test Stimulus Driver
Test and Debug interface driver
Quiescence
Other
Coherency
Reset Rules
Power Mgmt
Mem/Cache Models & Preloaders
End of Sim Detection
Control Register Interfaces
Performance
All Opcodes
Clock freq
Mem Req types
Mem Rsp types
CTL Reg modes
Inter-component Data Objects
Remember this slide?

## Slide 14: Drivers and Monitors
File with stimulus
File Reader
Stimulus Datastruct
Testbench Stimulus coordinator
Driver
DUT RTL
Monitor
Response Datastruct
Scoreboard
Reference Model
Pass/Fail
Response Datastruct
Remember this slide?
Notes: Maybe you can get rid of a lot of the pieces on the previous slide – but you still have to generate stimulus and check results.
But you certainly don’t need coverage checkers, and most of the signals in your monitors/checkers are inaccessible anyway.

## Slide 15: The weak link
What’s the weak link in post-Si verification speed?
  Remember: TB has 3x more code than the DUT
How do you make test generation fast?
  don’t generate tests on the fly. Or if you do…
  don’t rely on a compiler to generate tests
  assembler + test with lots of loops = better
  one test + lots of initial seeds = still better
How do you make results checking fast?
  reference model is previous silicon
  self-checking test (review: what is that?)
Notes: If you have enough computers handy, you could use 1000 machines to generate tests and put them on a very large disk… and then have the silicon platforms pull tests from that repository.
You still can’t keep up entirely, but you do get the months prior to silicon to build up that collection of tests…

## Slide 16: Fast vs. smart
Can trade off smarts for speed
Pre-silicon
  slow run-times
  invest in very smart test generation to make the most of those expensive cycles
Silicon
  dumb tests that are easy to generate
  but lots of them!

## Slide 17: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Debug hooks
Life in post silicon
Mock debug, war stories

## Slide 18: Problem #1 – repeatability
How do you debug your generic SW bugs?
  note you have a wrong answer, crash, etc.
  keep rerunning, work backwards to find the bug
Hidden assumption – you can rerun and see the exact same behavior
  i.e., your software is repeatable

## Slide 19: Is software really repeatable?
When has “debug-via-repeatable” not worked for you?
  memory bugs
  often have functionally different results on every run
  those are hard to debug!
What makes memory bugs so painful?
  rerunning any software → rarely see exact same timing
  what makes memory bugs worse?
Memory bugs are painful…
  because they break the particular flavor of repeatability you care about
  But why is this relevant to post-silicon?
Notes: Note that a host of ELECTRICAL issues can also cause non-repeatable behaviors
Slow rise/fall times due to loading can cause a signal to not meet timing, and OCCASIONALLY to not get latched by the next flop in time
Clock jitter
Multi-cycle paths
Temperature dependencies
Voltage level dependencies
Frequency dependencies
Capacitance
Noise (buck converters, R/F interference, …)

## Slide 20: What we care about
Programmer thinks HW is repeatable
  because they only care about results
  not about cycle-accurate timing
Timing is not repeatable!
  Time a program five times → get 5 (slightly) different times
Why doesn’t this break your SW debug?
Results are guaranteed by the architecture
  and the silicon works
  your re-runs see the same result every time – even with buggy SW
  Except for memory debug, multi-threaded debug
  any other interesting “except”s?
Notes: My other interesting “except”s: uninitialized variables

## Slide 21: Why is timing unpredictable?
Systems are big!
Many clock domains
  and clock crossings are hard to synch up
Reset is analog and hard to predict
Lots of big slow uncoordinated peripherals
  disk drives, DRAM
  DRAM refresh is hard to predict
Most of this can be corrected – but it’s hard
  a.k.a. thus expensive
Notes: Side note – learn to take advantage of system-level randomness as a source of randomness :-)

## Slide 22: Recap
Unpredictable timing is OK for SW debug on working HW (why?)
It’s not OK for HW debug (why?)
  different timings cause the bug to occur or not (occurs on DRAM refresh one cycle after cache miss…)
  Every rerun → a different bug!

## Slide 23: Problem #2 – visibility
Debugging with your favorite software IDE
  single step through programs (one line of code)
  observe the value of any variable
Debugging with SystemVerilog
  no single step (one clock cycle)
  you can still print any variable
Debugging silicon is different!
Notes: We’ll still have single step (see later), but it tends to make bugs vanish.
Note the difference between single step in the SW sense (i.e., one line of code) and in the HW sense (one clock cycle). You can get the former on a real system (we’ll talk about it soon).

## Slide 24: Visibility
Silicon has very little visibility 
  signals in your RTL may not exist (synthesis)
  wires are nm. long and flying by at GHz
  result – typically no way to see wire values!
You can still see the bumps
  they change quickly; a logic analyzer helps
  but that’s often not nearly enough
How can you possibly debug?
  No single step
  no print statement
  every rerun → different timing
Welcome to the brave new world of post-silicon debug hooks

## Slide 25: Problem #3 – can’t fix bugs
Pre-silicon
  debugging is (relatively) easy
  fixing a bug re-compiling (minutes, hours)
Post-silicon
  debugging can be quite hard
  fixing a bug requires a new silicon spin (months, $$$)
  !$#&*
  how can you deal with this?

## Slide 26: Focused Ion Beam
Shoots a focused ion beam(Gallium) at a target
  FIB can cut metal traces or dielectric
  Can deposit new wires
The features you want to change must be accessible!
Usually only practical for small numbers of changes
  Fibbed parts often don’t last long
  or run at speed

## Slide 27: Fixing bugs post-silicon
Software workaround
  Sometimes you can find a software workaround
  Might be slow & tedious and/or highly creative
  Lets you at least limp along to the next tapeout
Fixing more than a “small” number of bugs per stepping can be painful!
Alternate strategy: sells FPGAs and not ASICs 

## Slide 28: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Debug hooks
Life in post silicon
Mock debug, war stories

## Slide 29: Scan dumps
Q2
D Q
D Q
D Q
D Q
D Q
D Q
Logic
TDI
TDO
Mainly for manuf. test
You can fire them to take a very detailed snapshot
  Good – almost every flop on the chip)
  Bad – only one snapshot
  Ugly – when do you fire the clock?
Notes: TDI = Test Data In
TDO = Test Data Out

## Slide 30: One firing + non-repeatability
Why does it matter if a program takes a slightly different time at each run?
  The simplest way to trigger a scan dump is to count cycles from when the test is launched
  Non-repeatability in time means that won’t work!
So how can you debug?

## Slide 31: Better debug hooks
What do we really want?
A system that can
  fire a trigger 100M cycles before my bug happens
  capture every node on the chip
  for the next 100M cycles
  let us peruse all that data at our leisure
We probably could debug our chips with that 
But really, what can we actually get?

## Slide 32
How much area would that take?
  About as big as the entire chip!
  OK, what can we really live with?
How about every flop on the chip? Then just regenerate the other nodes
  That’s a scan dump. But we’ll still need the “100M cycles worth”
  Sorry, still too expensive
What about just the “important” nodes?
  Sure, but which ones are they?
  Sound like our functional-coverage problem?
  But we want the important nodes for debugging a bug that hasn’t happened yet 
Fire a trigger 100M cycles before my bug happens
Capture every node on the chip
For the next 100M cycles
Let us peruse all that data at our leisure

## Slide 33
Where do we store all of this data?
  Put a whole new memory onto the chip
  On-chip cache way
  Off-chip DRAM
  Debug port driving storage
Pros and cons of the above?
  Bandwidth vs. size
  Bumps are expensive and becoming relatively slower
  removing a cache way may remove your bug
Data→storage path may cross clock domains
Fire a trigger 100M cycles before my bug happens
Capture every node on the chip
For the next 100M cycles
Let us peruse all that data at our leisure
Unlikely
Notes: The larger-BW solutions typically have less available space.
As transistors scale faster than wires, bumps become slower (relative to gates) every generation. And we need more and more bumps for DRAM & other interfaces, leaving none for debug ports.
When your data crosses clock domains, you have extra unpredictability – it may corrupt important timing relationships.

## Slide 34
A debug system that predicts the future?
  We know what went wrong, but not the original cause
Make an educated guess what’s causing the bug, and turn that into a trigger?
  the bug doesn’t happen until after you have silicon
Make an educated guess about all the likely signals that might cause a bug 100M cycles in the future?
  Are you feeling lucky today?
Any good options at all?
Fire a trigger 100M cycles before my bug happens
Capture every node on the chip
For the next 100M cycles
Let us peruse all that data at our leisure

## Slide 35: Storage scope
trigger
How did the scope display 500ms of data before the trigger?

## Slide 36: Storage scope
Can you think of small number of signals that indicate a bug happened?
  branch to an exception handler
  test pokes a prearranged pin

## Slide 37
A debug system that predicts the future?
  We know what went wrong, but not the original cause
Continuously record data
  any useful data structures to continuously record into a finite-size buffer?
Wait for a trigger
Record n more cycles
Fire a trigger 100M cycles before my bug happens
Capture every node on the chip
For the next 100M cycles
Let us peruse all that data at our leisure
Notes: Where ‘n’ is fairly small, because things can go chaotic very quickly after a bug, and you don’t want to lose the 100M cycles you already gathered. And see below about the circular buffer – you may be overwriting old data.
What’s a good data structure to record continuously into a finite-size memory? Probably a circular buffer.

## Slide 38
Now it’s just a small matter of software 
  And of course you’re probably debugging this software at the same time as you’re debugging the chip
  Can build some IDE capabilities (single step; examine registers, cache & memory; replicate monitors)
  Single stepping can easily create a Heisenbug!
  Need all the monitors to beautify bits
Fire a trigger 100M cycles before my bug happens
Capture every node on the chip
For the next 100M cycles
Let us peruse all that data at our leisure
Notes: You build single step with the same software techniques as any IDE uses. You can look at SW variables (just like an IDE; they’re in memory). But of course you cannot look at arbitrary HW signals.
Cache dumps are usually via MBist and are quite useful.
Just like in pre-silicon verif, you need all the monitors to make lots of bits easy to understand by humans – but now those bits may not all be available 

## Slide 39: What you usually have
With a trigger:
  Scan dumps (but just one)
  Debugger (single step, examine registers & arrays)
  Signal tracing (trace a predetermined subset of signals with storage-scope functionality; different clock domains may not be aligned)
Defeatures, error injection
Writing custom tests

## Slide 40: Tension & debates
All of these debug hooks cost time and area!
  How many can you afford?
  You hope you’ll never need any of it!
  How much are you willing to pay to minimize schedule risk?
  How much insurance do you want to buy?

## Slide 41: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Debug hooks
Life in post silicon
Mock debug, war stories

## Slide 42: Typical schedule
Which milestone is most “important?”
  If your definition of “important” includes the company staying afloat…
  “time to other peoples’ money”
Tapeout 1
Tapeout 2
sales
all units coded
top-level assembled
concepts done
small team moves to next project
huge team comes onboard
team leaders write a paper
Remember this slide?

## Slide 43: Cost of a bug fix
Early in design: 1 engineer week ($5K)
Late in design: 1 week tapeout slip = $2M
  or 1 week = 1% performance
Post-silicon: 1 extra tapeout ($+2 months) = $20M
Post-FRS: lose 20% of your customers = $20M/year
After substantial field volume: recalls
  1995 Pentium fix = $495M
400x
4000x
100,000x
Remember this slide?
Notes: The issue: No more opportunity to mitigate this by rearranging future resources. Bugs often result in day-for-day revenue slips. High pressure!
Assume you’re selling a GPU; 1M units/year, $100/unit. so $100M/year or $2M/week
Hard to compute the cost of a tapeout (depends on your volume, etc and how many layers it involves). Scott’s numbers are $1M/layer, or $40M for a full-layer tapeout and $20M for metal-only. I’ll use $50M since Scott’s numbers are slightly old.

## Slide 44: Life under the hot lights
Pro: you get to be on a first-name basis with your CEO
Con – they’re trying to micromanage you without understanding your job
Con – it gets hot and sweaty under those lights!

## Slide 45: The ugly
One time, several years ago, I was called into a room with management and asked not only how long was it going to take to resolve the current bug we were working on, but also, how many more bugs we were going to have before the product was able to go into production. I tried to explain that if we knew how many bugs there were and how long they would take to resolve, we wouldn’t have put them there in the first place, but my explanation was just met with a room full of blank stares.
    The crazy mixed up world of silicon debug, Doug Josephson, 2005
Remember this slide?
Notes: The point – lots of pressure.
No place left to kick the can further down the road. The buck stops here.

## Slide 46: Life under the hot lights
Two shifts handing problems off
  Debug is a marathon, not a hundred-yard dash
  You own your career; your CEO doesn’t

## Slide 47: Outline of this lecture
Intro
Taking advantage of “fast”
Why debugging is hard
Debug hooks
Life in post silicon
Mock debug, war stories

## Slide 48: Exercise
The bug:
Your job – root-cause it!
The tools available: 20 questions
  You suggest a particular test (e.g., scan dump from trigger XXX)
  Invent triggers if needed
  You can only see the bumps (i.e., the interface between the mesh and the “verification environment”)
  We’ll tell you what your test showed

## Slide 49: Observations
Lack of visibility means
  make educated guesses based on indirect evidence to narrow down the cause of a bug
  lots of brainstorming, pulling in experts
Use defeatures to narrow down causes
  or to create artificial stress (turn a once-in-80-hours bug into a once-in-80-seconds bug)
  queue-size reduction, error injection

## Slide 50: Issue #1
Packets are getting dropped

## Slide 51
# Starting the sim! # T=180: launching packet #0, Data= 7, valid=1, from y,x=(0,0) -> (2,2) # T=180: launching packet #1, Data= 1, valid=1, from y,x=(1,0) -> (2,2) # T=200: launching packet #2, Data=14, valid=1, from y,x=(2,2) -> (3,2) # T=200: launching packet #3, Data= 2, valid=1, from y,x=(1,0) -> (2,2) # T=220: launching packet #4, Data= 5, valid=1, from y,x=(0,0) -> (2,2) # T=220: launching packet #5, Data= 9, valid=1, from y,x=(1,2) -> (2,2) # T=240: launching packet #6, Data= 4, valid=1, from y,x=(0,1) -> (2,2) # T=240: launching packet #7, Data= 5, valid=1, from y,x=(2,2) -> (3,2) # 1. T=260: data_avail_for_venv[3][2]; Data=14, valid=1, from y,x=(2,2) -> (3,2), packet #2 # T=260: launching packet #8, Data= 1, valid=1, from y,x=(2,1) -> (2,2) # T=260: launching packet #9, Data= 8, valid=1, from y,x=(0,1) -> (2,2) # T=280: launching packet #10, Data=13, valid=1, from y,x=(0,3) -> (2,2) # T=280: launching packet #11, Data= 6, valid=1, from y,x=(2,1) -> (2,2) # 2. T=280: data_avail_for_venv[2][2]; Data= 9, valid=1, from y,x=(1,2) -> (2,2), packet #5 # 3. T=300: data_avail_for_venv[2][2]; Data= 1, valid=1, from y,x=(1,0) -> (2,2), packet #1 # 4. T=300: data_avail_for_venv[3][2]; Data= 5, valid=1, from y,x=(2,2) -> (3,2), packet #7 # T=300: launching packet #12, Data=15, valid=1, from y,x=(3,0) -> (2,2) # T=300: launching packet #13, Data=10, valid=1, from y,x=(1,1) -> (2,2) # T=320: launching packet #14, Data= 2, valid=1, from y,x=(0,3) -> (2,2) # T=320: launching packet #15, Data= 4, valid=1, from y,x=(2,1) -> (2,2) # 5. T=320: data_avail_for_venv[2][2]; Data= 7, valid=1, from y,x=(0,0) -> (2,2), packet #0 # 6. T=340: data_avail_for_venv[2][2]; Data= 2, valid=1, from y,x=(1,0) -> (2,2), packet #3 # T=340: launching packet #16, Data=13, valid=1, from y,x=(2,0) -> (2,2) # T=340: launching packet #17, Data=14, valid=1, from y,x=(3,0) -> (2,2) # T=360: launching packet #18, Data= 9, valid=1, from y,x=(3,1) -> (2,2) # T=360: launching packet #19, Data= 8, valid=1, from y,x=(0,2) -> (2,2) # 7. T=360: data_avail_for_venv[2][2]; Data= 5, valid=1, from y,x=(0,0) -> (2,2), packet #4 # 8. T=380: data_avail_for_venv[2][2]; Data= 4, valid=1, from y,x=(0,1) -> (2,2), packet #6 # T=380: launching packet #20, Data= 9, valid=1, from y,x=(1,2) -> (2,2) # T=380: launching packet #21, Data=11, valid=1, from y,x=(1,1) -> (2,2) # T=400: launching packet #22, Data= 4, valid=1, from y,x=(3,1) -> (2,2) # T=400: launching packet #23, Data= 0, valid=1, from y,x=(1,0) -> (2,2) # 9. T=400: data_avail_for_venv[2][2]; Data= 8, valid=1, from y,x=(0,1) -> (2,2), packet #9 # 10. T=420: data_avail_for_venv[2][2]; Data=13, valid=1, from y,x=(2,0) -> (2,2), packet #16 # T=420: launching packet #24, Data=12, valid=1, from y,x=(1,0) -> (2,2) # T=420: launching packet #25, Data= 3, valid=1, from y,x=(3,1) -> (2,2) # T=440: launching packet #26, Data=10, valid=1, from y,x=(1,0) -> (2,2) # T=440: launching packet #27, Data= 1, valid=1, from y,x=(3,1) -> (2,2) # 11. T=440: data_avail_for_venv[2][2]; Data= 8, valid=1, from y,x=(0,2) -> (2,2), packet #19 # 12. T=460: data_avail_for_venv[2][2]; Data= 9, valid=1, from y,x=(1,2) -> (2,2), packet #20 # T=460: launching packet #28, Data=13, valid=1, from y,x=(3,1) -> (2,2) # T=460: launching packet #29, Data=15, valid=1, from y,x=(3,2) -> (2,2) # T=480: launching packet #30, Data= 8, valid=1, from y,x=(0,1) -> (2,2) # T=480: launching packet #31, Data= 2, valid=1, from y,x=(0,3) -> (2,2) # 13. T=480: data_avail_for_venv[2][2]; Data=13, valid=1, from y,x=(0,3) -> (2,2), packet #10 # 14. T=500: data_avail_for_venv[2][2]; Data=15, valid=1, from y,x=(3,0) -> (2,2), packet #12 # T=500: launching packet #32, Data= 6, valid=1, from y,x=(1,3) -> (2,2) # T=500: launching packet #33, Data=14, valid=1, from y,x=(3,3) -> (2,2) # T=520: launching packet #34, Data=11, valid=1, from y,x=(0,3) -> (2,2) # T=520: launching packet #35, Data= 4, valid=1, from y,x=(1,0) -> (2,2) # 15. T=520: data_avail_for_venv[2][2]; Data= 2, valid=1, from y,x=(0,3) -> (2,2), packet #14 # 16. T=540: data_avail_for_venv[2][2]; Data=14, valid=1, from y,x=(3,0) -> (2,2), packet #17 # T=540: launching packet #36, Data= 7, valid=1, from y,x=(0,3) -> (2,2) # T=540: launching packet #37, Data=10, valid=1, from y,x=(0,0) -> (2,2) # T=560: launching packet #38, Data=11, valid=1, from y,x=(0,0) -> (2,2) # T=560: launching packet #39, Data= 6, valid=1, from y,x=(2,1) -> (2,2) # 17. T=560: data_avail_for_venv[2][2]; Data=15, valid=1, from y,x=(3,2) -> (2,2), packet #29 # 18. T=580: data_avail_for_venv[2][2]; Data= 0, valid=1, from y,x=(1,0) -> (2,2), packet #23 # T=580: launching packet #40, Data= 3, valid=1, from y,x=(0,3) -> (2,2) # T=580: launching packet #41, Data= 7, valid=1, from y,x=(0,0) -> (2,2) # T=600: launching packet #42, Data= 8, valid=1, from y,x=(0,3) -> (2,2) # T=600: launching packet #43, Data= 5, valid=1, from y,x=(0,2) -> (2,2) # 19. T=600: data_avail_for_venv[2][2]; Data=12, valid=1, from y,x=(1,0) -> (2,2), packet #24 # 20. T=620: data_avail_for_venv[2][2]; Data=10, valid=1, from y,x=(1,0) -> (2,2), packet #26 # T=620: launching packet #44, Data= 8, valid=1, from y,x=(0,1) -> (2,2) # T=620: launching packet #45, Data=10, valid=1, from y,x=(2,2) -> (3,2) # T=640: launching packet #46, Data= 7, valid=1, from y,x=(0,0) -> (2,2) # T=640: launching packet #47, Data= 4, valid=1, from y,x=(2,3) -> (2,2) # 21. T=640: data_avail_for_venv[2][2]; Data=10, valid=1, from y,x=(1,1) -> (2,2), packet #13 # 22. T=660: data_avail_for_venv[2][2]; Data= 9, valid=1, from y,x=(3,1) -> (2,2), packet #18 # T=660: launching packet #48, Data=14, valid=1, from y,x=(0,3) -> (2,2) # T=660: launching packet #49, Data=15, valid=1, from y,x=(2,0) -> (2,2) # Done launching packets! # 23. T=680: data_avail_for_venv[2][2]; Data= 5, valid=1, from y,x=(0,2) -> (2,2), packet #43 # 24. T=680: data_avail_for_venv[3][2]; Data=10, valid=1, from y,x=(2,2) -> (3,2), packet #45 # 25. T=700: data_avail_for_venv[2][2]; Data= 2, valid=1, from y,x=(0,3) -> (2,2), packet #31 # 26. T=720: data_avail_for_venv[2][2]; Data= 6, valid=1, from y,x=(1,3) -> (2,2), packet #32 # 27. T=740: data_avail_for_venv[2][2]; Data=14, valid=1, from y,x=(3,3) -> (2,2), packet #33 # 28. T=760: data_avail_for_venv[2][2]; Data=11, valid=1, from y,x=(0,3) -> (2,2), packet #34 # 29. T=780: data_avail_for_venv[2][2]; Data= 3, valid=1, from y,x=(0,3) -> (2,2), packet #40 # 30. T=800: data_avail_for_venv[2][2]; Data= 8, valid=1, from y,x=(0,3) -> (2,2), packet #42 # 31. T=820: data_avail_for_venv[2][2]; Data= 4, valid=1, from y,x=(2,3) -> (2,2), packet #47 # 32. T=840: data_avail_for_venv[2][2]; Data= 4, valid=1, from y,x=(1,0) -> (2,2), packet #35 # 33. T=860: data_avail_for_venv[2][2]; Data=14, valid=1, from y,x=(0,3) -> (2,2), packet #48 # 34. T=880: data_avail_for_venv[2][2]; Data=10, valid=1, from y,x=(0,0) -> (2,2), packet #37 # 35. T=900: data_avail_for_venv[2][2]; Data=11, valid=1, from y,x=(0,0) -> (2,2), packet #38 # 36. T=920: data_avail_for_venv[2][2]; Data= 7, valid=1, from y,x=(0,0) -> (2,2), packet #41
# 37. T=940: data_avail_for_venv[2][2]; Data= 7, valid=1, from y,x=(0,0) -> (2,2), packet #46 # 38. T=960: data_avail_for_venv[2][2]; Data=15, valid=1, from y,x=(2,0) -> (2,2), packet #49 # 39. T=980: data_avail_for_venv[2][2]; Data= 4, valid=1, from y,x=(3,1) -> (2,2), packet #22 # 40. T=1000: data_avail_for_venv[2][2]; Data= 8, valid=1, from y,x=(0,1) -> (2,2), packet #30 # 41. T=1020: data_avail_for_venv[2][2]; Data= 3, valid=1, from y,x=(3,1) -> (2,2), packet #25 # 42. T=1040: data_avail_for_venv[2][2]; Data= 1, valid=1, from y,x=(3,1) -> (2,2), packet #27 # 43. T=1060: data_avail_for_venv[2][2]; Data= 8, valid=1, from y,x=(0,1) -> (2,2), packet #44 # 44. T=1080: data_avail_for_venv[2][2]; Data= 1, valid=1, from y,x=(2,1) -> (2,2), packet #8 # 45. T=1100: data_avail_for_venv[2][2]; Data= 6, valid=1, from y,x=(2,1) -> (2,2), packet #11 # 46. T=1120: data_avail_for_venv[2][2]; Data= 4, valid=1, from y,x=(2,1) -> (2,2), packet #15 # 47. T=1140: data_avail_for_venv[2][2]; Data= 6, valid=1, from y,x=(2,1) -> (2,2), packet #39 # Stopping simulation due to timeout; not all packets received

## Slide 52: Issue #2
Performance is poor
  All packets are correctly delivered – but about 3x slower than expected

## Slide 53: War stories
Notes: Scott’s War stories:
Capacitance on package
Capacitive coupling
Undersized transistor driver
Power virus
Reset
“Dead rat” B0
If only I could remember the details of the buck converter

## Slide 54: Backup
Optical probing
Tester vs. system debug

## Slide 55: Post-Si Debug Methodologies (pg. 1)
Deterministic Replay
  Asynchronous clocks introduce non-determinism
  Requires an extremely small reproducible set of stimulus
  Requires “Run N” and ATPG type DFT (scan capabilities)
    MISR Signatures
Backspace (Freeze on Fail and Speculate)
  Iteratively surmise the necessary states and pre-conditions
  Effective for Hangs
  Otherwise, Inaccurate and Difficult
  Good for characterization with ample time and visibility

## Slide 56: Post-Si Debug Methodologies (pg. 2)
On-the-Fly Analysis
  Best with Low MTTF, Difficult with High MTTF failures
    Large number of test systems needed for statistical MTTF
  Requires Scan on the Fly infrastructure OR….
  Environmental Experimentation (turn stuff off)
    Defeatures, Chicken Bits, Traffic modulators Required
History Capture (Logic Analyzers, Trace Buffers)
  Area – Large Arrays needed for capture depth
  Power Consumption
  Complexity
  Security
  Cross Design-Object Triggering
  Time Correlation